## Slide 1
Milano, XX mese 20XX
Relatore: Prof. Maurizio Quadrio
INCREASING THE PARALLEL EFFICIENCY OF A SOLVER FOR THE DIRECT NUMERICAL SIMULATION OF TURBULENCE
Mirco Meazzo - 873477

## Slide 2: Why?
Mirco Meazzo - 873477
Although we are surrounded all day long by fluids, like the air that we breathe, we do not know much about their behaviour.
This happens because we do not dominate the "secrets" of the turbulence
A better understanding of the turbulence phenomena/s is mandatory if we want to reduce the power needed to stream through fluids, thus reducing our footprint on the environment.
An example of practical implications of a better understanding of the phenomena/s could potentially lead to safer and more efficient transportation systems

## Slide 3: The Direct Numerical Simulation
Mirco Meazzo - 873477
In order to get an insight of the turbulence phenomena the only way towards knowledge is the direct numerical simulation (DNS) of the Navier-Stokes equations.
This computational technique does not involve turbulence models, therefore requires exceptional computational power in order to investigate all spatial scales, from the dissipative ones up to the integral length.
Industry
Academy
DNS
LES
RANS
Notes: f(wave#), Re^3

## Slide 4: High Performance Computing
Mirco Meazzo - 873477
The solution is rely in HPC, however, to exploit the theoretical performances we must design the solver using a parallel strategy

## Slide 5: Distribuited Shared Memory
Mirco Meazzo - 873477
Our goal was to realize a massively parallel solver, starting from the original low-parallelized implementation
MPI Technology
Starting point: "A low-cost parallel implementation of direct numerical simulation of wall turbulence", P. Luchini and M. Quadrio, JCP (2005)
Notes: Basato su ark a memoria distribuita,
? Realizzare questo sys Efficiente e semplice?
MPI:
Libreria che contiene un insieme di funzioni pensate per gestire la comunicazione tra processori appartenenti alla stessa rete

## Slide 6: Distribuited Shared Memory
Mirco Meazzo - 873477
Paradigm Pros:
Scales well with a large number of nodes
Provides large virtual memory space
No need to replicate data
Use cheaper hardware
Paradigm Drawbacks:
Message passing latency
Bandwidth limitations
Difficult troubleshooting
Notes: Vantaggi di questo modello di programmazione
Principale possibilità di scalare elevato n nodi

## Slide 7: Solver Features
Mirco Meazzo - 873477
Written partially in CPL and partially in C
Based on Fourier expansion series along homogenous directions
Compact finite differences along wall normal direction
Convolutions computed in time domain to reduce computational cost
Massively parallel thanks to MPI implementation
1D or 2D domain decomposition
MPI
fftMPI
Array Transpose
Communication
Notes: Il nostro solutore è caratterizzato da..
Use estensivo delle seguenti librerie esterne,
…Grazie all’uso di fftMPI

## Slide 8: Domain Decomposition
Mirco Meazzo - 873477
Notes: decomposizione 2D arrays,
consente maggiore scalabilità del codice,
sposta limite teorico scaling,
prodotto tra i 2 modi più piccoli

## Slide 9: Scaling Performance (1/2)
Mirco Meazzo - 873477
128x128x128 Grid
256x256x512 Grid
Notes: Benchmark, S=t_single/t_p
128^3 cpl vs mpi
Mentre Decomp 1D non presenta sensibilità al #CORES
256x256x512 f(CORES)

## Slide 10: Scaling Performance (2/2)
Mirco Meazzo - 873477
256x256x512 Grid
Speedup vs Mesh Size
Notes: Su suggerimento del Cineca -> adottato Intel 18,
Autovettorizzazione codice
Picco Scaling f(#modi)
Hyperthreading poco efficace,

## Slide 11: Validation
Statistics
Mirco Meazzo - 873477
Where:
Viscous Sublayer
Buffer Region
Logarithmic Region
Notes: Validare solutore, Re=5600
Legge di parete: brevemente …,
Aritmetica moderna >> KMM 1986
Tau_w= wall shear stress

## Slide 12: Comparison
Mirco Meazzo - 873477
Notes: Panoramica legge parete,
U_mean
Componenti sforzo di taglio (channel_units) al var di RE
…Re2000
8miliardi di gdl, ½ TB per step

## Slide 13: Interest in Increasing
Mirco Meazzo - 873477
Increasing is fundamental to provide a better separation among layers, therefore it become simpler to distinguish energy dissipating scales from energy containing scales.
If is very large exist an intermediate layer in which the profile of depends on the viscous length alone. In this layer the behaviour of assumes the typical logarithmic profile
Comparative data from "Direct Numerical Simulation of Turbulent Channel Flow up to ", Moser and Lee, JFM(2015)
Notes: se log -> B=1/K (K=Von Karman)

## Slide 14: Particular Fluctuations Behaviour
Mirco Meazzo - 873477
Can we spot particular behaviours also in streamwise and spanwise fluctuations?
Notes: Aggiungere slide intro su towsend con
Funzione Predittore andamento logaritmico

## Slide 15: Simulations Results
Mirco Meazzo - 873477
Spanwise fluctations term exhibit logaritmic behaviour
Streamwise fluctuations term is close to develop a logarithmic behaviour
Higher Re needed
Notes: Funzione Predittore andamento logaritmico

## Slide 16: Conclusions
OpenMP implementation is recommended to increase the efficiency of the solver over present and future clusters families processors
Mirco Meazzo - 873477
BUT,
Today’s market trend has moved from «Raise Clock Frequency» towards «Raise the cores number»
Possibility to handle very large simulations
Good scalability reached

## Slide 17: Titolo presentazione sottotitolo
Milano, XX mese 20XX
Thanks for the attention
… And these unforgettable years!